## Slide 1: EFFECTS OF FIREWORKS ON THE AIR QUALITY IN BUDAPEST
ELTE Eötvös Loránd University, Budapest
Institute of Chemistry
Faculty of Science
Felipe Reis Fernandes
MSc Diploma Thesis Defence
Supervisor: Dr. Salma Imre

## Slide 2: Introduction
Firework History: From China 10th Century to Europe 17th Century
Popular in many events:
  China: New Year
  India: Diwali
  USA: Independence Day
  Hungary: Saint Stephen’s Day
Saint Stephen’s Day: 20th August, Budapest
  30 min usually
  City Center along Danube
  2021 – One of the largest events in Europe
Notes: On events mention only saint Stephen’s day

## Slide 3: Fireworks
Composition:
  Metals: Color (Sr, Ba, Cu), Fuel (Mg, Al, Zn)
  Fuel: C (black carbon, sugar), S, P
  Oxidants: (per)chlorates, nitrates
Pollution:
  O3, SO2, NOx, CO , Aerosols
  Particles containing metals, toxic organic compounds
  WHO (UF): 1 h mean > 20k cm-3 – High
Goals:
  Characterize air pollution of the event
  Particle number concentration and size distribution
  Possible influence of meteorological conditions
Notes: On Composition no need to discriminated each element, rather only the 3 main groups
On pollution focus on the aerosol/particles, no need to mention the others

## Slide 4: Methods
Years: 2009, 2014, 2015, 2016,2017, 2020 and 2021
From 20:00 to 23:30
  Before Time (BT): 20:00 to 21:00
  During Time (DT): 21:00 to 22:00
  After Time (AT): 22:30 to 23:30
Location: BpART Lab (yellow dot)
Measurements:
  Differential Mobility Particle Sizer (DMPS) – Concentration and size distribution
  Condensation Particle Counter (CPC) – Total concentration
  WS, WD, T and RH – Meteorological Parameters
Data treatment:
  Descriptive statistics
  Welch’s t-test for mean comparison (two side: α= 0.1, one side: α=0.0.5)
  RDiff: Relative Difference of Means
  Z-value: Relative mean difference to standard deviation

## Slide 5: Results and Discussion
2021 as base:
  Size ranges
  Time intervals
Initial pattern recognition with contour plots
Descriptive statistics
  Central tendencies and distribution
Particle size distribution and proportions
Event and non-event comparisons

## Slide 6: 2021 Day Parameters

## Slide 7: CPC (N6-1000)

## Slide 8: 2020

## Slide 9: 2021

## Slide 10: Particle Size Distribution (2021)

## Slide 11: Relative Particle Size Distribution

## Slide 12: Particle Size Change (2009, 2014, 2015)

## Slide 13: Particle Size Change (2016,2017,2020,2021)

## Slide 14: z-value

## Slide 15: Welch’s t-test one sided

## Slide 16: Conclusion
Most of the particles produced are within 40 and 400 nm
Weather conditions can change the detectability of the event
Using other tools such as scattered sensors, drones, checking for trace metals could improve the data collected
Fireworks generate a beautiful spectacle that do not last for long time
Very intensive events can generate pollution levels harmful for Human health
Intercalating or substituting fireworks with lights and drones can bring the pollution to safety levels

## Slide 17: Thank you

## Slide 18: Additional Material

## Slide 19: Mean Comparison
RDiff
z-value

## Slide 20: Charges over Danube 2021

## Slide 21: DMPS

## Slide 22: Descriptive Statistics
 | Parameter | 2009 | 2014 | 2015 | 2016 | 2017 | 2020 | 2021
BT | N6–100 | 16 | 8.0 | 9.2 | 6.5 | 6.5 | 6.1 | 24
 | N100–1000 | 3.5 | 2.1 | 1.7 | 2.1 | 0.7 | 1.4 | 5.2
 | WS | 2.0 | 0.7 | 3.6 | 1.4 | 5.2 | 0.8 | 0.5
 | WD | 130 | 32 | 44 | 166 | 15 | 102 | 120
 | T | 24 | 19 | 19 | 26 | 21 | 25 | 24
 | RH | 40 | 73 | 61 | 61 | 49 | 52 | 55
DT | N6–100 | 22 | 11 | 8.8 | 12 | 4.3 | 7.2 | 22
 | N100–1000 | 7.6 | 3.8 | 2.1 | 8.2 | 0.5 | 1.7 | 57
 | WS | 10 | 0.7 | 4.4 | 1.1 | 4.4 | 1.2 | 1.4
 | WD | 180 | 30 | 45 | 159 | 9 | 101 | 116
 | T | 22 | 19 | 19 | 25 | 19 | 24 | 22
 | RH | 46 | 77 | 64 | 65 | 48 | 58 | 62
AT | N6–100 | 26 | 14 | 6.6 | 17 | 6.2 | 7.1 | 18
 | N100–1000 | 82 | 4.6 | 1.8 | 3.5 | 0.7 | 1.9 | 4.6
 | WS | 2 | 0.9 | 3.9 | 0.9 | 3.7 | 0.9 | 0.8
 | WD | 110 | 28 | 44 | 28 | 37 | 143 | 122
 | T | 20 | 18 | 18 | 24 | 18 | 23 | 22
 | RH | 58 | 83 | 67 | 70 | 53 | 64 | 63

## Slide 23: RDiff

## Slide 24: CPC Welch’s t-test – Total Particles
Time Frequency | Years | Two-Sided BD | Two-Sided AD | One-Sided BD | One-Sided AD
1s | 2020 | 0.0 | 1.3 × 10-08 | 0.0 | 6.4 × 10-09
 | 2021 | 0.0 | 0.0 | 0.0 | 0.0
30s | 2020 | 1.7 × 10-13 | 0.26 | 8.4 × 10-14 | 0.13
 | 2021 | 5.1 × 10-17 | 2.3 × 10-18 | 2.6 × 10-17 | 1.1 × 10-18
1min | 2020 | 2.3 × 10-08 | 0.38 | 1.1 × 10-08 | 0.19
 | 2021 | 4.1 × 10-09 | 9.2 × 10-10 | 2.0 × 10-09 | 4.6 × 10-10